This tutorial will guide the user trhough the conversion of coarse grain simulations to atomisitic.
This tutorial assumes that the users has some basic knowledge of GROMACS, martini coarsegrain and atomistic representations.

The goal of CG2AT2 is the production of a ready to run atomistic system, including all forcefield topologies and itp files. The script will produce a set of core folders; INPUT, MERGED and FINAL as well as a set of folders for each residue type.

INPUT:
Contains all the input files provided to the script.

MERGED:
Contains the merged system. The system minimisation, NVT and Steering occurs here.

FINAL:
Conatins all the files needed to run your atomistic simulation.

Residue folder e.g. POPG
Contains all the conversion files for the residue type

LspA tutorial
The protein we will work on is the LspA protein. An equilibrated CG system can be found in folder “cg2at/tutorials/LspA_tutorial/input_files”, with all the following commands are assumed to be run from: “cg2at/tutorials/LspA_tutorial”

De novo conversion

To convert the CG system into the de_novo, all that is required is the CG system file. This can be in any form which is recognised by “gmx editconf” which are: gro, g96, pdb, brk, ent, esp and tpr

Execute CG2AT2 by issuing the following command:

Python ../../cg2at.py -c input_files/CG_input.pdb

Now the script will ask you several questions about which fragment library, forcefield and water model to use just enter the option and press enter. For this tutorial we will use charmm36, therefore we will select: the forcefield “charmm36-mar2019-updated”, the corresponding fragment library “martini_2-0_charmm36” and the water model “tip3p”.

These can be specfied in the input command by using the flags -fg, -ff and -w.

e.g.
python ../../cg2at.py -ff charmm36-mar2019-updated -fg martini_2-0_charmm36 -w tip3p -c input_files/CG_input.pdb

Hopefully CG2AT2 will have run successfully and will have produced a folder called CG2AT appended with the current time. Within this folder will be all of the conversion folders, in the FINAL directory all of the files required to carry on the simulation can be found.

Aligned conversion

To include create a aligned system, we need to supply a reference atomistic structure. This is done with the flag “-a”, the atomistic segments can be placed in a single file or supplied in separate files. As with the previous flag “-c” they can be in any form which is recognised by “gmx editconf” which are: gro, g96, pdb, brk, ent, esp and tpr.

Here we will automate the process as described above by specifing the libraries to use, as well as including the refeernce structure with the flag “-a”.

Execute CG2AT2 by issuing the following command:

python ../../cg2at.py -ff charmm36-mar2019-updated -fg martini_2-0_charmm36 -w tip3p -c input_files/CG_input.pdb -a input_files/AT_input.pdb

With the addition of the atomistic structure a distance restraint matrix is applied to the de_novo structure during the de_novo NVT step. This improves the conversion of the de novo as it helps orientate the amide bonds to the correct plane.